# Hardware Overview

## zactrack mini specific hardware

### MASTER Anchor
Product number: z00309101
Material: ABS (IP 50)
Dimensions: 190 x 207 x 36 mm
Gross Weight: 680 g
Power Supply: DC 5.1V 3A
Battery: 3.7V, 5200mAh, Li-Ion battery (3h battery life, 3 hours charging time)
Ports: 1 LAN, 1 USB-C for Power, 1 XLR for DMX512 Output
Mounting: Rig mounting plate for clamp and safety line
Explanation of the numbering:
1. LED - Operation light
2. Screwing Attachment (1/4“ inch thread for tripod)
3. LED - Power status
  1. green: battery full
  2. yellow: battery half full
  3. red: battery <10%
  4. red blinking: empty
4. Power button
  1. Short press: show battery
  2. Log press: switch ON / OFF
5. USB-C port
6. Ethercon port (LAN)
7. DMX port

### Anchor
Product number: z00301101
Material: ABS (IP 54 - with closed USB-C connector)
Dimensions: 140 x 140 x 35 mm
Weight: 290 g
Power Supply: DC 5.1V 3A
Battery: 3.7V, 2600mAh, Li-Ion battery (16h battery life, 2 hours charging time)
Mounting: Rig mounting plate for clamp and safety line
Explanation of the numbering:
1. LED - Operation light
2. Screwing Attachment (1/4” inch thread for tripod)
3. LED - Power status
  1. green: battery full
  2. yellow: battery half full
  3. red: battery <10%
  4. red blinking: empty
4. Power button
  1. Short press: show battery
  2. Log press: switch ON / OFF
5. USB-C port

### Tracker
Product number: z00302101
Material: ABS (IP65)
Dimensions: 35 x 60 x 10 mm
Weight: 26 g
Battery: 3.7V, 310mAh, LiPO battery
Battery Operating Time: 4 hours (active) / 20 hours (inactive)
Charging: 2 hours (100%), DC 5V 0.2A
### Charging Station
Product number: z00203101
Material: ABS
Dimensions: 270 x 70 x 70 mm
Weight: 390 g
Connection: USB-C, DC 5V 1A
### Disks
Material: ABS
Dimensions: 57 x 57 x 20 mm
Colors: Green, blue, red, and white
## Additional hardware
Besides the specific zactrack hardware it is also necessary to use the following additional hardware to run zactrack MINI.
Android Tablet necessary for setup process

## Technology
Radio RTLS (Real Time Location System) based on Decawave DWM1001
Accuracy: < 10 cm
Update Rate: 15 Hz (Setting: 5 active trackers - depends on number of active trackers)
Connectivity: UWB (Ultra Wideband) channel 5 - 6,2 - 6,7 GHz, 500 MHz bandwidth
Default radio channel: channel 5 / 6,5 GHz
Radio regulations: Ultra-Wideband worldwide radio regulations
https://www.decawave.com/sites/default/files/apr001_uwb_worldwide_regulations_summaryrev1.2.pdf
Wi-Fi
Connectivity: 2.4GHz (channels 1 - 11) / 5GHz (channels 36, 38, 40, 44, 46, 48)
Default Frequency: 2.4GHz
Default Wi-Fi channel: channel 7