# Set up the zactrack Puck

zactrack Puck
### Connect zactrack Puck to zactrack WIFI
- Turn on the zactrackPuck with the switch at the bottom.
- The LED indicates the state (green flashing -> connected to network)
- The zactrackPuck is now ready for fixture alignment
Note: If the LED indicates blue continiously -> no known wifi network is found and own zactrackPuck WIFI will be enabled. Klick the following link to configuration_of_zactrack_puck_wifi_network

### Recommended settings of zactrack Puck
- Setup ip address: 192.168.4.1
- Recommended ip address: 172.20.1.211
- Standard Gateway: 172.20.1.1
- Subnet: 255.255.0.0
### Configuration of zactrack Puck WIFI network
If the LED shines continous blue search for a zactrackPuck network on your device.
1. Connect your device to the network and wait for a few seconds.
2. A pop-up brings you to the zactrackPuck config window. (You can type 192.168.4.1 in your browser to go there manually)
3. Press the Button to scan for availabe networks.
4. Choose a network by tapping on it or entering the SSID.
   Put in the password and tap save.
   Note: If your desired network is not shown you can hit the scan button to rescan or enter the SSID and password manually.

1. List of all available networks (Standard WIFI -> “zactrack”)
2. Credentials of chosen network
3. zactrack Puck network settings (default settings should remain unchanged)
If the configuration succeeded the following dialog comes up: