# Network

#### Network Port 1: zacNET
IP range	172.20.xx.xx
Subnet	255.255.0.0

- All anchors are connected to zacNET
- WIFI Access Point is connected to zacNET
  Note: To set up the WIFI access point please go to Set up the WIFI network

#### Network Port 2: sACN, ArtNet, PSN, OSC
Standard IP	192.168.0.200
Subnet	255.0.0.0

Note: Change the ip address of Port 2 in Advanced Settings / System Config
- sACN (streaming ACN)
  ACN (and streaming ACN) is an ANSI/ESTA international standard.
  For additional information about this protocol please read:
  http://en.wikipedia.org/wiki/Architecture_for_control_networks
- Art-Net support of Art-Net 1, 2
  Art-Net is a royalty free protocol developed by Artistic Licence
  For additional information about this protocol please read:
  http://www.artisticlicence.com
- PSN
  PosiStageNet or PSN is a open protocol developed by MA Lighting and VYV Corporation
  For additional information about this protocol please read:
  http://www.posistage.net
- OSC
  Open Sound Control (OSC) is a protocol for communication among computers, sound synthesizers, and other multimedia devices
  For additional information about this protocol please read:
  http://opensoundcontrol.org