# Hardware Overview

## zactrack specific hardware

### Anchor
Product number: z00101101
Material: ABS (IP 54)
Dimensions: 190 x 150 x 38 mm
Weight: 500 g
Power Supply: PoE (48V) - CAT6 compatible with Neutrik etherCON
Mounting: Aluminium Plate for Clamps incl. rig for safety line
Technology: Radio RTLS (Real Time Location System) based on Decawave DW1000
Accuracy: < 10 cm
Update Rate: 1 - 25 Hz
Connectivity: UWB (Ultra Wideband) channel 1 - 3, 3,5 - 4,5 GHz, 500 MHz bandwith
Default radio channel: channel 3 / 4243.2 – 4742.4 GHz
Radio regulations: Ultra-Wideband worldwide radio regulations
https://www.decawave.com/sites/default/files/apr001_uwb_worldwide_regulations_summaryrev1.2.pdf
Channels and Bandwidths
UWB Channel Number	Centre Frequency (MHz)	Band (MHz)	Bandwidth (MHz)
1	3494.4	3244.8 – 3744	499.2
2	3993.6	3774 – 4243.2	499.2
3	4492.8	4243.2 – 4742.4	499.2

### Tracker (Transmitter)
Product number: z00102101
Material: ABS
Dimensions: 47 x 33 x 7,5 mm
Weight: 15,4 g
Battery Operating Time: -> 4,5 hours in tracking mode / multiple days in standby mode
Charging: 2 hours (100%), 5V DC
### Tracker Charger

Product number: z00102191
Material: ABS
Dimensions: 295 x 235 x 20 mm

### zactrack Puck
Product number: z00107101
Material: ABS
Dimensions: 95mm Ø x 35mm
Weight: 200g
Battery: 2x AA -> 12 hours
### zactrack SERVER
Product number: z00109201
Case: 19-inch rack 1U, Half-length
Form Factor: 19“ 1U chassis
Motherboard: X10SDV-TP8F
Dimensions: 43 x 437 x 249 mm
Gross Weight: 5 kg
Power Supply: 230VA with Input 100 - 240Vac, 91% efficiency
AC Input Frequency: 50-60Hz
Buttons: Power On/Off button, System Reset Button
LEDs: 2 Network Activity LEDs, Fan Fail/System Over Heat LED, HDD activity LED, Power Status LED
Ports: 1x VGA, IPMI, 4xLANs, 1x COM, 4xUSB, 1xKeyboard/Mouse
### zactrack TABLET
Samsung Galaxy Tab S7 FE:
Dimensions: 18,5 x 28,48 x 0,63 cm
Screen: 12.4 Zoll, 16:9, 2560×1600, Multi-Touch
Wireless: WLAN 802.11a/​b/​g/​n/​ac, Bluetooth 4.2
Weight: 610g
Battery: 10090mAh,
Connector: USB-C
Samsung Galaxy Tab S8:
Dimensions: 16,53 x 25,38 x 0,63 cm
Screen: 11 Zoll, 16:9, 2560 x 1600, Multi-Touch,
Wireless: WLAN 802.11a/​b/​g/​n/​ac, Bluetooth 4.2
Weight: 503g
Connector: USB-C
## Additional hardware
Besides the specific zactrack hardware it is also necessary to use the following additional hardware to run zactrack.
- PoE switch to power and link all anchors into one network
  - Managed switch
  - >10W per port
  - Recommended products: https://www.luminex.be/products/gigacore/
- CAT6 ethernet cables for the anchors and connections between switches
- Leica DISTO S910 incl. tripod head and tripod (https://lasers.leica-geosystems.com/disto/s910)
- WIFI Access Point with this configuration