# Add universes
- Go to Show Editor
- Tap in section “Universes” to add a new universe
- Type in a unique name of the universe and tap on Create
- Choose Input or Output universe
- Choose ArtNet or sACN and type in the appropriate universe
  - ArtNet
    - Broadcast: 2.255.255.255
    - Unicast: Type in the ip address of the appropriate network listener (Ethernet/DMX Node)
      Note: Universe starts at 0.0
  - sACN
    - Multicast
    - Unicast: Type in the ip address of the appropriate network listener (Ethernet/DMX Node)
- Toggle In Merge and choose the appropriate IN Universe if you have also additional fixtures patched in the universe which you don't use for following.
  -> All channels coming from this IN Universe will be rerouted to this created OUT universe
- Tap Ok