#### Auto 6M Use Full Console Range
There are two different ways of how the multipliers are calculated, depending on whether or not the advanced property in the System Settings is enabled or not.
##### Option 1: Property "Auto 6M Use Full Channel Range" is enabled:
Let autovalue be the value calculated based on autofunctions/smart zoom and consolevalue the one received from the console on the fixture's input universe. Furthermore, let dmxfullrangemin and dmxfullrangemax be the theoretical dmx value limits, regardless of the limits set in the fixture's fixture type. Then the final channel value finalvalue is calculated by using the following formula:
multiplicator = 2 * ((console_value - dmx_full_range_min) / (dmx_full_range_max - dmx_full_range_min))
final_value = auto_value * multiplicator
For example, consider a fixture with an 8-bit IRIS channel (theoretical DMX values of 0-255), but a limited dmx range defined in its fixture type (e.g. DMX values of 0-131). With Auto 6M mode active...
- ...sending an IRIS value of 0 (0 % of theoretical dmx range) from the lighting console leads to the final IRIS value being 0, regardless of autofunctions or other factors (due to the multiplicator being 0 as well).
- ...sending an IRIS value of 127 (50 % of theoretical dmx range) from the lighting console leads to the final IRIS value being exactly the same as autovalue (due to the multiplicator being 1).
- ...sending an IRIS value of 255 (100 % of theoretical dmx range) from the lighting console leads to the final IRIS value being twice as big as autovalue (due to the multiplicator being 2).
##### Option 2: Property "Auto 6M Use Full Channel Range" is disabled:
Let autovalue be the value calculated based on autofunctions/smart zoom and consolevalue the one received from the console on the fixture's input universe. Furthermore, let dmxmin and dmxmax be the dmx limits as specified in the fixture's fixture type. Then the final channel value finalvalue is calculated by using the following formula:
multiplicator = 2 * ((console_value - dmx_min) / (dmx_max - dmx_min))
final_value = auto_value * multiplicator
For example, consider a fixture with an 8-bit IRIS channel (theoretical DMX values of 0-255), but a limited dmx range defined in its fixture type (e.g. DMX values of 0-131). With Auto 6M mode active...
- ...sending an IRIS value of 0 (0 % of limited dmx range) from the lighting console leads to the final DIMMER value being 0, regardless of autofunctions or other factors (due to the multiplicator being 0 as well).
- ...sending an IRIS value of 65 (50 % of limited dmx range) from the lighting console leads to the final IRIS value being exactly the same as autovalue (due to the multiplicator being 1).
- ...sending an IRIS value of 131 (100 % of limited dmx range) from the lighting console leads to the final IRIS value being twice as big as autovalue (due to the multiplicator being 2).
- ...sending an IRIS value of 255 (195 % of limited dmx range) from the lighting console leads to the final IRIS value being almost four times as big as autovalue (due to the multiplicator being 3.9).