# Universes
zactrack is able to send and receive the following network DMX protocols:
- ArtNet
- sACN
  Note: A zactrack mini system can send out one universe via physical XLR (which is marked with ).
  Additional universes can be sent via Ethernet (sACN, ArtNet).

### Add universes
- Tap on Universes in the Show Editor
- Tap to add a new universe
- Type in a unique name of the universe and tap on Create
- Choose Input or Output universe
- Choose ArtNet or sACN and type in the appropriate universe
  - ArtNet
    - Broadcast: 2.255.255.255
    - Unicast: Type in the IP address of the appropriate network listener (Ethernet/DMX Node)
      Note: Universe starts at 0.0
  - sACN
    - Multicast
    - Unicast: Type in the IP address of the appropriate network listener (Ethernet/DMX Node)
- Toggle In Merge and choose the appropriate IN Universe if you also have additional fixtures patched in the universe which you don't use for following.
  -> All channels coming from this IN Universe will be rerouted to this created OUT universe
- Tap Ok
- Tap and tap upload to server
  Note: Upload to server will affect the current show
- shows successful upload
### Universe traffic monitoring
- Tap on Universes in the Show Editor
- Tap on on the right side of the specific universe you want to monitor
  Note: You can monitor both IN and OUTPUT universes