# MOUNT
- Mount the 8 anchors around the stage. The positions of the anchors should be as asymmetrical as possible, for good resolution in 3D 4 anchors should be up and 4 down.
- Connect the zactrack CORE (Server ETHERNET PORT1) to a network switch
- Connect the anchors with a CAT6 cable to a PoE switch within the zacNET
  Note:
  LED on anchor illuminates blue -> anchor has power and is connected to tracking server
  LED on anchor red -> anchor has power but no connection to tracking server

  Max. length of CAT6 with PoE is 100m. It is possible to extend the range with fiber optic cables
- Connect the zactrack CORE (Server ETHERNET PORT2) to the lighting network switch
### 3D Anchor Setup
All anchors should be mounted around stage on different heights. To get accurate Z-axes positions it is necessary to mount the anchors on multiple Z-levels. Below you will find 2 examples for a 3D anchor setup.
For a 3D position the system picks at least 4 anchors.
Note: You can change the tracking type from 2D to 3D direct on each tracker on the lightconsole

Note: Do not place an anchor directly next to a fixture

### 2D Anchor Setup
All anchors should be mounted around stage. For 2D anchor setup it is NOT necessary to mount the anchors on multiple Z-levels. Below you will find 2 examples for a 2D anchor setup.
For a 2D position the system picks at least 3 anchors.